## Slide 1: Combinational Logic Sequential Logic CPU Datapath
CMPT 295 Week 10

## Slide 2: Synchronous Digital Systems (SDS)
Synchronous:
  All operations coordinated by a central clock
    “Heartbeat” of the system (processor frequency)
Digital:
  Represent all values with two discrete values
  Electrical signals are treated as 1’s and 0’s
    High/Low voltage represent True/False, 1/0
Hardware of a processor (e.g., RISC-V) is an example of a Synchronous Digital System

## Slide 3: Combinational vs. Sequential Logic
Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    Example: add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    Also called “State Elements”
    Example: Memory and registers

## Slide 4: Simple Logic Gates
Special names and symbols:
NOT
AND
OR
a | b | a AND b
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
a | b | A OR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
a | NOT a
0 | 1
1 | 0
Circle means NOT!
= NOT a
= a AND b
= a OR b
True if input is false
True if both inputs are true
True if at least one input is true
Truth Table
4

## Slide 5: More Simple Logic Gates
Inverted versions are easier to implement in CMOS
NAND
NOR
XOR
a | b | a NOR b
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
a | b | a XOR b
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
a | b | a NAND b
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
= a NAND b
= a NOR b
= a XOR b
True if both inputs are false
True if exactly one input is true
(or if odd number of inputs are true for > 2 inputs)
True if at least one input is false

## Slide 6: Computing with Combinational Circuits
Definition: A combinational circuit computes a pure function, i.e., its outputs react only based on its inputs. There are no feedback loops and no state information (memory) is maintained.
Theorem: Every Boolean function can be implemented with NAND and NOT. Circuits are modular
FA
FA
FA
FA
A3
B3
A2
B2
A1
B1
A0
B0
S3
S2
S1
S0
C3
C2
C1
C0
C4
… a 4-bit ripple carry adder!
  Adds by columns
  Propagation delay
= 9
(2n + 1)
Adder-4
A
B
4
4
4
S
C
C
Notes: Orally: We used to spend ⅔ of CMPT 150 on the design techniques to minimize circuit size, gate delay, etc …
The point in CMPT 295 is only that it is possible to do so, and that gate delay is a thing
Orally: This is why additions is slow. And why mul is even slower.
Orally: How to make an Adder-8?

## Slide 7: Combining Multiple Logic Gates
A
B
C
D
D = (NOT(A AND B)) AND (A OR (NOT B AND C))

## Slide 8: How to Represent Combinational Logic?
Text Description
Circuit Diagram
  Transistors and wires
  Logic Gates
Truth Table
Boolean Expression
All are equivalent

## Slide 9: Useful Combinational Circuits

## Slide 10: Data Multiplexor (MUX)
Multiplexor (“MUX”) is a selector
  Place one of multiple inputs onto output (N-to-1)
Shown below is an n-bit 2-to-1 MUX
  Input S selects between two inputs of n bits each
This input is passed to output if selector bits match shown value
Represents that this input has n bits
A
B
S
0
1
C
‘n
‘n
‘n

## Slide 11: Implementing a 1-bit 2-to-1 MUX
Schematic:
Truth Table:
Boolean Algebra:
Circuit Diagram:
s | a | b | c
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
A
B
S
0
1
C
‘n
‘n
‘n
s

## Slide 12: 1-bit 4-to-1 MUX
Schematic:
Truth Table: How many rows?
Boolean Expression: E = S1S0A + S1S0B + S1S0C + S1S0D
26
A
D
S= S1S0
00
11
E
‘2
01
10
B
C

## Slide 13: Another Design for 4-to-1 MUX
Can we leverage what we’ve previously built?
  Alternative hierarchical approach:
A
B
0
1
C
D
S0
0
1
S1
0
1
E

## Slide 14: Decoder
Enable one of 2N outputs based on N input
Example: 2-to-4 decoder
Use case: Choose ALU operation based on instruction op-code
By BlueJester0101, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=3668293

## Slide 15: Demultiplexer (Demux)
Similar to decoder with an enable signal
By BlueJester0101, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=3668293

## Slide 16: Single-Bit Binary Adder (Half Adder)
Add A + B to get Sum (S) and Carry (C)
Truth Table:
Boolean Expressions:
  S = AB; C = AB
Circuit:
By inductiveload - Own work, Public Domain, https://commons.wikimedia.org/w/index.php?curid=1023090
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 17: What is this Circuit?
S = A ⊕ B ⊕ C; C = AB + C(A ⊕ B)
0
1
1
0
1
0
0
1
Truth table:
A B C
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0
0
0
1
0
1
1
1
3-bit
Addition!
A
B
C
Q. What’s the propagation delay?
C
S
3 gate delays (highlighted)
Q. What does the circuit accomplish?
Algebra:
S = A ⊕ B ⊕ C
C S
Full Adder
Half Adder
Half Adder
FA
S
C
C
A
B

## Slide 18: Functional Unit
FS func
0001 A + B
0010 A − B
1000 A * B
0100 A ^ B
0101 A + 1
1101 B
32
Hardware circuits are fixed
Can’t adjust wires / gates while running
Build control wires to parametrize its function
Function Unit:
32
opA
32
opB
res
4
FS
Function Select:

## Slide 19: Functional Unit: Adder-Subtractor
32
Adder-32
32
32
A
32
B
S
C
FS
if FS == 0 then
S = A + B
if FS == 1 then
= A − B
S = A + B + 1

## Slide 20: Combinational vs. Sequential Logic
Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL)
    Output is a function of the inputs only, not the history of its execution
    Example: add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    Also called “State Elements”
    Example: Memory and registers

## Slide 21: Sequential Logic

## Slide 22: Digital State Machines
Memory holds state information
memory
combinational
circuit
current
state
inputs
next state
outputs
compute next state based on (current state, inputs)
compute outputs based on (current state, inputs)
Q. What does this imply about the clock period?
clock period must exceed (tpd of combinational circuit + tpd of registers) where tpd is propagational delay

## Slide 23: Accumulator Example
Want: S=0;
for X1,X2,X3 over time...
S = S + Xi
An example of why we would need sequential logic
Assume:
  Each X value is applied in succession, one per cycle
  The sum since time 1 (cycle) is present on S
SUM
Xi
S

## Slide 24: First Try: Does this work?
No!
How to control the next iteration of the ‘for’ loop?
How do we say: ‘S=0’?
Feedback
X
+
S

## Slide 25: Second Try: How About This?
A Register is the state element that is used here to hold up the transfer of data to the adder
Xi
+
S
register
Load/Clk
reset

## Slide 26: Accumulator Revisited: Proper Timing
Reset signal shown
In practice Xi might not arrive to the adder at the same time as Si-1
Si temporarily is wrong, but register always captures correct value
In good circuits, instability never happens around rising edge of CLK
Xi
+
Si
register
Clk
reset
Si-1
“Undefined” (unknown) signal
X0
X0+X1
X0+X1+X2
X0+X1+X2+X3
X0
X1
X2
X3
Xi
Si
0
X0
X0+X1
X0+X1 +X2
Si-1
Reset
CLK

## Slide 27: Maximum Clock Frequency
Max Delay =
Min Period = Max Delay
Max Freq = 1/Min Period
CLK-to-Q Delay
+ CL Delay
+ Setup Time
Assumes Max Delay > Hold Time
Notes: Hold time is included in CLK-to-Q delay.
Make sure to shift thinking for setup time for next clock trigger (one clock cycle).

## Slide 28: The Critical Path
+
Reg
Reg
The critical path is the longest delay between any two registers in a circuit
The clock period must be longer than this critical path, or the signal will not propagate properly to that next register

## Slide 29: How do we go faster?
Pipelining!
Split operation into smaller parts and add a register between each one.

## Slide 30: Uses for State Elements
Place to store values for some amount of time:
  Register files (like in RISCV)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements are used to hold up the movement of information at the inputs to combinational logic blocks and allow for orderly passage

## Slide 31: RISC-V CPU Datapath, Control Intro
Notes: Podcast link: https://gimletmedia.com/tags/6dug/super-tech-support

## Slide 32: Design Principles
Five steps to design a processor:
  Analyze instruction set → datapath requirements
  Select set of datapath components & establish clock methodology
  Assemble datapath meeting the requirements
  Analyze implementation of each instruction to determine setting of control points that effects the register transfer
  Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 33: Summary !
Universal datapath
  Capable of executing all RISC-V instructions in one cycle each
  Not all units (hardware) used by all instructions
5 Phases of execution
  IF (Instruction Fetch), ID (Instruction Decode), EX (Execute), MEM (Memory), WB (Write Back)
  Not all instructions are active in all phases (except for loads!)
Controller specifies how to execute instructions
  Worth thinking about: what new instructions can be added with just most control?

## Slide 34: Your CPU in two parts
Central Processing Unit (CPU):
  Datapath: contains the hardware necessary to perform operations required by the processor
    Reacts to what the controller tells it! (ie. “I was told to do an add, so I”ll feed these arguments through an adder)
  Control: decides what each piece of the datapath should do
    What operation am I performing? Do I need to get info from memory? Should I write to a register? Which register?
    Has to make decisions based on the input instruction only!

## Slide 35: Design Principles
Determining control signals
  Any time a datapath element has an input that changes behavior, it requires a control signal (e.g. ALU operation, read/write)
  Any time you need to pass a different input based on the instruction, add a MUX with a control signal as the selector (e.g. next PC, ALU input, register to write to)
Your control signals will change based on your exact datapath
Your datapath will change based on your ISA

## Slide 36: Storage Element: Register File
Register File consists of 31 registers:
  Output ports portA and portB
  Input port portW
Register selection
  Place data of register RA (number) onto portA
  Place data of register RB (number) onto portB
  Store data on portW into register RW (number) when Write Enable is 1
Clock input (CLK)
  CLK is passed to all internal registers so they can be written to if they match RW and Write Enable is 1
Clk
portW
Write Enable
32
32
portA
32
portB
5
5
5
RW
RA
RB
32 x 32-bit
Registers

## Slide 37: Implementing R-Types
IMEM
+4
ALU
pc
inst[11:7]
inst[19:15]
inst[24:20]
Control
New hardware: ALU (Arithmetic Logic Unit)
Abstraction for adders, multipliers, dividers, etc.
How do we know what operation to execute?
  Our first control bit! ALUSel(ect)
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
R[rs1]
R[rs2]
ALUSel
inst[31:0]
31
0
func7(7)
opcode(7)
rs2(5)
rs1(5)
Func3(3)
rd(5)
7 6
12 11
15 14
20 19
25 24

## Slide 38
Inst[31:0] |  |  |  |  |  |  |  |  | ALUSel |  | 
add |  |  |  |  |  |  |  |  | Add |  | 
sub |  |  |  |  |  |  |  |  | Sub |  | 
(R-R Op) |  |  |  |  |  |  |  |  | (Op) |  | 

## Slide 39: Adding addi to datapath
Control Logic
+4
pc
pc+4
inst[11:7]
inst[19:15]
inst[24:20]
IMEM
inst[31:0]
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Reg[rs1]
Reg[rs2]
alu
ALU
ALUSel=Add
Imm.
Gen
0
1
RegWEn=1
inst[31:20]
imm[31:0]
ImmSel=I
BSel=1
Also works for all other I-format arithmetic instruction (slti,sltiu,andi,ori,xori,slli,srli,srai) just by changing ALUSel

## Slide 40
Inst[31:0] |  | ImmSel |  |  |  |  | BSel |  | ALUSel |  | 
add |  | * |  |  |  |  | Reg |  | Add |  | 
sub |  | * |  |  |  |  | Reg |  | Sub |  | 
(R-R Op) |  | * |  |  |  |  | Reg |  | (Op) |  | 
addi |  | I |  |  |  |  | Imm |  | Add |  | 

## Slide 41: Adding lw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=I
RegWEn=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=0
wb

## Slide 42
Inst[31:0] |  | ImmSel |  |  |  |  | BSel | ASel | ALUSel | MemRW | WBSel
add |  | * |  |  |  |  | Reg | Reg | Add | Read | ALU
sub |  | * |  |  |  |  | Reg | Reg | Sub | Read | ALU
(R-R Op) |  | * |  |  |  |  | Reg | Reg | (Op) | Read | ALU
addi |  | I |  |  |  |  | Imm | Reg | Add | Read | ALU
lw |  | I |  |  |  |  | Imm | Reg | Add | Read | Mem

## Slide 43: Storage Element: Idealized Memory
Memory (idealized)
  One input port: Data In
  One output port: Data Out
Memory access:
  Read: Write Enable = 0, data at Address is placed on Data Out
  Write: Write Enable = 1, Data In written to Address
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read, behaves as a combinational logic block: Address valid → Data Out valid after “access time”
CLK
Data In
Write Enable
32
32
DataOut
Address

## Slide 44: Current Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:20]
ALU
mem
wb
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
BSel
ALUSel
MemRW
WBSel
wb
pc+4

## Slide 45: Adding sw to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
0
1
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
pc+4
Reg[rs1]
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=S
RegWEn=0
Bsel=1
ALUSel=Add
MemRW=Write
WBSel=*
wb
*= “Don’t Care”

## Slide 46
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
add | +4 | * | 1 (Y) | * | * | * | Reg | Reg | Add | Read | ALU
sub | +4 | * | 1 | * | * | * | Reg | Reg | Sub | Read | ALU
(R-R Op) | +4 | * | 1 | * | * | * | Reg | Reg | (Op) | Read | ALU
addi | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | ALU
lw | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | Mem
sw | +4 | S | 0 (N) | * | * | * | Imm | Reg | Add | Write | *

## Slide 47
Inst[31:0] | PCSel | ImmSel | RegWEn | BrUn | BrEq | BrLT | BSel | ASel | ALUSel | MemRW | WBSel
add | +4 | * | 1 (Y) | * | * | * | Reg | Reg | Add | Read | ALU
sub | +4 | * | 1 | * | * | * | Reg | Reg | Sub | Read | ALU
(R-R Op) | +4 | * | 1 | * | * | * | Reg | Reg | (Op) | Read | ALU
addi | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | ALU
lw | +4 | I | 1 | * | * | * | Imm | Reg | Add | Read | Mem
sw | +4 | S | 0 (N) | * | * | * | Imm | Reg | Add | Write | *
beq | +4 | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
beq | ALU | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
bne | ALU | B | 0 | * | 0 | * | Imm | PC | Add | Read | *
bne | +4 | B | 0 | * | 1 | * | Imm | PC | Add | Read | *
blt | ALU | B | 0 | 0 | * | 1 | Imm | PC | Add | Read | *
bltu | ALU | B | 0 | 1 | * | 1 | Imm | PC | Add | Read | *
jalr | ALU | I | 1 | * | * | * | Imm | Reg | Add | Read | PC+4
jal | ALU | J | 1 | * | * | * | Imm | PC | Add | Read | PC+4
auipc | +4 | U | 1 | * | * | * | Imm | PC | Add | Read | ALU

## Slide 48: Adding branches to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=B
RegWEn=0
BrUn
BrEq
BrLT
ASel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=*
PCSel=taken/not-taken
wb

## Slide 49: Adding jalr to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=B
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=0
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb

## Slide 50: Adding jal to datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=J
RegWEn=1
BrUn=*
BrEq=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=Read
WBSel=2
PCSel
wb

## Slide 51: Implementing lui
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=*
Bsel=1
ALUSel=B
MemRW=Read
WBSel=1
PCSel=pc+4
wb
pc

## Slide 52: Implementing auipc
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel=U
RegWEn=1
BrUn=*
BrE=*
BrLT=*
Asel=1
Bsel=1
ALUSel=Add
MemRW=0
WBSel=1
PCSel=pc+4
wb
pc