## Slide 1: Multi-Layer Video Broadcasting with Low Channel Switching Delays
Cheng-Hsin Hsu
Joint work with Mohamed Hefeeda
Simon Fraser University, Canada

## Slide 2: Mobile TV
Watch TV anywhere, and anytime
  users: watch more programs
  providers: higher revenues
Broadcast over cellular networks
  Inefficient, because they are: (i) designed for unicast, and (ii) narrowband
Several standards for dedicated broadcast networks
  DVB-H, MediaFLO, T-DMB

## Slide 3: Different from Regular TV
Heterogeneity among mobile devices
Energy is critical: battery powered
  In cellular phones, about 40% energy consumption is due to mobile TV chips
    measurements on Nokia N96 phones
  Broadcast standards dictate mechanisms to save energy

## Slide 4: Energy Saving for Mobile Devices
This is called time slicing (in DVB-H and MediaFLO)
Base station constructs a time slicing scheme
  (time, size) for bursts of individual TV channels
Time
R
r
Off
Burst

## Slide 5: Channel Switching Delay
Time slicing increases channel switching delay
Low switching delays are important
  Long delays are annoying
  Users flip through too many channels
User switches
channel
Burst
Device gets
the video data

## Slide 6: Problem Statement
Design a time slicing scheme to support heterogeneous mobile devices, such that
  Each mobile device has an energy consumption proportional to its received video quality
  Channel switching delays on all mobile devices are bounded by , which is a system parameter
But, how to support heterogeneous devices?
  For example, devices with different display resolutions?

## Slide 7: Support Heterogeneous Devices
Multi-version: encode each video into several versions, and concurrently broadcast them
  Simple, but not efficient
  Spectrum is expensive
Multi-layer: encode each video into a scalable stream consists of several layers, and broadcast each layer only once
  Bandwidth efficient, but challenging in mobile TV broadcast networks

## Slide 8: Mobile TV Base Station and Frame Format
MPE Frame
Video
Server
IP
Encapsulator
Modulator
IP pkts
IP/MPE
frames
RF
signal
R-S Data Table
64 Columns
App. Data Table
191 Columns
256, 512, 768, or
1024 Rows
Packet 1
P. 2
P. 2
P. 3
P. 3
Padding
FEC Bytes Computed
Row-by-Row

## Slide 9: An Illustrative Example: Challenge
OK for devices that receive both layers
Picture 1
Layer 1
Picture 1
Layer 2
Picture 2
Layer 1
Picture 2
Layer 2
Padding
FEC Bytes Computed
Row-by-Row
Picture 3
Layer 1
Picture 3
Layer 1
Picture 3
Layer 2
BAD for devices that only receive the base layer
Higher energy consumption

## Slide 10: Our Solution: Layer-Aware Transmission
Base station properly organizes the video data while broadcasting
Mobile devices that only receive the base layer can skip the enhancement layer
  reduce energy consumption

## Slide 11: Layer Aware Time Slicing Scheme (LATS)
Burst time for layer c of channel s is:
  where b is burst size, R is network bandwidth
Time
Rate
Channel 1
Layer 1
Channel 1
Layer 1
Channel 1
Layer 2
Channel 2
Layer 1
Channel 2
Layer 2
Channel 3
Layer 1
Channel 3
Layer 2

## Slide 12: Performance of LATS
Lemma 1, 2:
Devices that receive c layers achieve
energy saving:
  Smaller c values result in higher energy saving
a worst case channel switching delay:
  Independent to c values, but…

## Slide 13: Problem of LATS
Delays are reduced by choosing a smaller b
  b = 200 kb  7.5 sec delay  40% energy saving
Can we do better?
May incur high
switching
delays

## Slide 14: LATS with Delay Bound (LATSB)
Our Idea: inserting frequent and short bootstrap bursts between two LATS bursts
Bootstrap bursts carries base layers
Bootstrap
Bursts
Time
Normal
Bursts
Optimized
for
Low Delays
Optimized
for High
Energy saving

## Slide 15: Performance of LATSB
Lemma 3:
Devices that receive c layers achieve
energy saving (with normal bursts):
  Smaller c values result in higher energy saving
a worst case channel switching delay:
  Independent to c values, and…

## Slide 16: Low Switching Delays of LATSB
Let b = 1500 kb, LATSB reduces delay from 60 sec (LATS) to less than 200 msec

## Slide 17: Empirical Evaluation
Implement LATS and LATSB schemes in a real base station
Encode each video into an SVC stream with four layers
  Each layer has a bit rate of 192 kbps
Broadcast four TV channels
Emulate a million mobile devices, and randomly generate channel switching events
  On average, 60 sec per channel watch time

## Slide 18: Cumulative Received Data
Current: always receive complete streams
LATS, LATSB: devices may opt for partial streams

## Slide 19: Energy Saving
LATS, LATSB enable a range of energy saving: up to 95%

## Slide 20: Channel Switching Delay
LATSB significantly reduces the switching delays

## Slide 21: Conclusion
Studied the problem of broadcasting TV channels to mobile devices with diverse resources
Proposed and analyzed two time slicing schemes
Implemented them in a real mobile TV base station
Empirically showed that
  LATS, LATSB support heterogeneous mobile devices
  LATS, LATSB achieve high energy saving
  LATSB achieves low channel switching delay

## Slide 22: Questions?
More details can be found online at
  http://nsl.cs.sfu.ca

## Slide 23: Implication of Average Watch Time on LATSB
Curves shown for devices receiving all layers
Energy saving is > 70% except extreme cases